Dusty’s Construction

& Handyman Service

Located in Willow Glen @:

972 Spadafore Ct.

San Jose CA 95125

Phone # 408.394.5260

Web-site: dustysconstruction.com

Lic. # 360004

Toni Lee									5/10/10

2036 Glen Una

San Jose CA 95125

267-8441

Re: Concrete & Stonework @ Above Location

Scope of Work:

Stock site with tools and materials

Remove all tools and equipment from site

Windshield and buying materials time

(Approx. 3 hours X 2 men)

Demolition:

(a)

@ Wrought Iron Man Gate:

Set up tools

Remove wrought iron gate by pulling pins (if possible). Or, drape as needed.

Chip uneven concrete surfaces flat for saw cuts

Diamond saw approx 9’ of concrete and remove to other job dumpster

Chip/cut existing 4x4 old wood post down to sub grade or as needed for overlay

Cut existing grade down to sub grade for underlayment

Remove all dirt to other planter areas before concrete chip contamination

Chip around existing 4x4 iron post for overlay

Roll up tools and Clean up

(Approx. 5-6 hours X 2 men.

(b)

@ Rear corner of house in planter area

Remove existing pavers/stepping stones

Cut existing grade down to sub grade for underlayment

Remove all dirt to other planter areas before concrete chip contamination

(Approx. 3 hours X 2 men)

(c)

@ Rear overlaid walkway from driveway to grass

Wire brush remove grouting slop over from curbs and slab (if possible)

(Approx. ½ hour X 2 men)

New Construction:

(For ‘a’ Above)

Set up tools and materials 4 times

Set bordering material using Owner’s material (On site)

Mix and pour concrete underlayment 2 ½-3” thick and float

Mix Thinset and set stone to finish elevation and sponge clean

Mix grout and grout all to finish elevation and sponge clean

Re-hang gate if needed

Roll up and clean up four times

(Approx. 7 hours X 2 men)

(For ‘b’ Above)

Set up tools and materials four times

Set bordering material using Owner’s material (On site)

Mix and pour concrete underlayment 2 ½-3” thick and float

Cut and set front walk and porch type green stone mesh assemblies to borders, curbs, & existing overlaid slab

Mix Thinset and set stone to finish elevation and sponge clean

Mix grout and grout all to finish elevation and sponge clean

Roll up and clean up four times

(Approx. 5 hours X 2 men)

(For ‘c’ Above)

Acid wash this area and sponge off

Rinse area and sponge off

(Approx. 2 hours for one man)

Additional Repairs To existing:

(1)

Remove existing broken 1x4x6’ redwood stop from front gate and replace.

(2)

Remove broken zone valve solenoid at front of house and replace

(Hopefully one hour for one man)

(Note: The above estimated hours add up to 54 hours, while my bid below only reflects 42 hours @ 20.00 per hour. If my estimated hours are close to correct, then the bid below only nets 15.50 per hour.)

Bid Amount:

Materials: (Note; Owner to pay materials

Labor:

For (a) above:									440.00

For (b) above:									320.00

For (c) above:									  60.00

For 1&2 above:								  20.00

Total:										840.00

Payment Schedule:

Upon Signing:									      420.00

Upon Completion:					    			      420.00

Total:										      840.00

________________________________________________________________________ Toni Lee                Date:                            Richard Gartner             Date: